## Slide 1: OCTA-based Assessment of morphological changes in active mCNV during anti-VEGF therapy
Paper Summary by Aadit Deshpande

## Slide 2: Introduction
Purpose:
  Profile quantitative changes of mCNV lesion using OCTA and explore biomarkers that could reflect outcome of VEGF inhibition.
mCNV:
  Myopic choroidal neovascularization (type 2 CNV) threatens vision.
  5-11% of individuals with Pathologic Myopia develop mCNV.
Treatment:
  Anti-vascular endothelial growth factor (VEGF) intravitreal injection.
Diagnosis:
  Standard Method: Fluorescein Angiography [dye-leakage risks]
  Alternative: OCTA (optical coherence tomography angiography) [non-invasive, quantitative assessment.]

## Slide 3: Patient Demographics, Data Acquisition
31 eyes (29 patients between Feb 2017 and Oct 2020 )
Subgroup Analysis:
Stable group (1 or 2 injections)
Unstable group (>2 injections)
OCTA Imaging using a commercial SD-OCT system.
Provided 4 en-face images (superficial and deep layers).

## Slide 4: OCTA Image Assessment
Quantitative Estimation
MATLAB & ImageJ program to process OCTA images:
  Manual Delineation
  Denoising (Gaussian kernel)
  Frangi vesselness Filter
  Local Adaptive Thresholding
  Skeletonization
Establish OCTA biomarkers.
Qualitative Estimation
Two mCNV phenotypes:
  Organized Interlacing
  Disorganized Vascular Loops
Morphology described by 5 criteria.
Organized Interlacing:
  Medusa
  Sea-Fan
  Tree-In-Bud

## Slide 5: Quantitative Estimation
Figure | Stage | OCTA Biomarker
A | Input image | 
B | Manual Delineation | mCNV Area
C | Gaussian Blur | 
D | Local Thresholding | Vessel Area
E | Skeletonization | Fractal Dimension, Tortuosity
F | Skeleton Analysis | Junctions, Vessel Length

## Slide 6: Results
Biomarkers After anti-VEGF treatment:
Moderate Correlation 4 between OCTA Biomarkers (mA, FD, VA, VL) and CRT
Organized Interlacing mCNV: (A, B) Baseline (C, D) Post Therapy
Decreased: mCNV Area Fractal Dimension Vessel Area Vessel Length Vessel Junction CRT (Central Retinal Thickness) | Increased: Vessel Density Vessel Diameter Tortuosity

## Slide 7: Statistical Analysis
Highlighted Biomarkers reported an increase post-treatment.

## Slide 8: Conclusion
Distinguished Two subtypes of mCNV (Organized interlacing and Disorganized vascular loops)
MATLAB and ImageJ to analyze morphological, spatial vessel biomarkers.
Anti-VEGF safe and efficacious treatment:
  Vessel junctions (-50.36%)
  Vessel length (-37.07%)
Challenges: Segmentation errors artifacts for highly myopic patients.
Limitations:
  1. Small sample size and short follow-up period.
  2. Measurement accuracy compromised by automation.

## Slide 9: Thank You